## Slide 1: iCub3 Forearm joints specs
Rev. 1
22/02/2016

## Slide 2: JOINTS 0– Forearm pronosupination
-Motor type: DC
-Motor encoder: 512 ppr
-Harmonic drive: 1/100
-No encoder at the joint
-HW limits roll (±90°)

## Slide 3: Wrist yaw & pitch – coupled joints
-Motor type: DC
-Motor encoder: 400 ppr
-Integrated gearbox 1/159
-Cables’pulleys reduction 14/ 18.8
- AEA at both joints
-HW limits ±45°

## Slide 4: Thumb, index and middlef. proximals
-Motor type: DC
-Motor encoder: 10 ppr
-Integrated gearbox 1/256
-Pulleys reduction n.a.
- Hall effect sensor at the joint

## Slide 5: Thumb distals - 2 joints 1 motor
-Motor type: DC
-Motor encoder: 10 ppr
-Integrated gearbox 1/256
-Pulleys reduction n.a.
- Hall effect sensor at the joints

## Slide 6: Index distals - 2 joints 1 motor
-Motor type: DC
-Motor encoder: 10 ppr
-Integrated gearbox 1/256
-Pulleys reduction n.a.
- Hall effect sensor at the joints

## Slide 7: Middlefing. distals - 2 joints 1 motor
-Motor type: DC
-Motor encoder: 10 ppr
-Integrated gearbox 1/256
-Pulleys reduction n.a.
- Hall effect sensor at the joints

## Slide 8: Ring and pinky distals - 4 joints 1 motor
-Motor type: DC
-Motor encoder: 10 ppr
-Integrated gearbox 1/256
-Pulleys reduction n.a.
- Hall effect sensor at the joints

## Slide 9: Fingers abduction
-Motor type: DC
-Motor encoder: no
-Integrated gearbox 1/256
-Pulleys reduction n.a.
- Hall effect sensor at the joint

## Slide 10: Thumb abduction
-Motor type: DC
-Motor encoder: no
-Integrated gearbox 1/256
-Pulleys reduction n.a.
-Hall effect sensor at the joint